Powering on the CNC
- Power on the machine by turning the emergency stop button on the front
- Unlock the alarm in the gcode sender toolbox
- Run the “home all” macro

Before starting the job
- When changing the stock or the cutter it is wise to power off the mill with
   the emergency button on the front. Better safe than sorry.
- Mount the stock to the t-slot table with clamps. Use at least 2 clamps,
  preferably more. Do not over tighten the clamps as that may deform the
  stock.
  If you planning to cut out your workpiece from the stock put a spoil board
  underneath the stock to protect the table.
- Mount the cutter you are about to use in the spindle and tighten with the
  wrenches.
- Before every start of a job use the jog controller to position the spindle
  above the toolsetter and run the “Probe Z” macro with the cutter you are
  about to use in the spindle. If the table is to be Z=0 put the toolsetter on the
  table, if the top of the stock is to be Z=0 put it on the stock.
- Use the jog controller to set the X and Y to the location they should be on
  the stock. Some Gcode starts at 0,0 in the lower left corner, some starts
  with 0,0 in the center. Use the visualizer to check.
- Use the jog controller or “outline” from the program menu to move to the
  minimum and maximum X and Y and make sure nothing is in the way for
  the job.
- Make sure the GCODE you generated will start the spindle, this is done
  with the command “M3” followed by the rpm in the GCODE. Check this
  in the GCODE window or your GCODE generator.

When something goes wrong.
- Is it minor, like a position that is incorrect then hit “pause” or “stop” in the
  gcode sender and correct the issue.

WITH ANY OTHER ISSUE HIT THE EMERGENCY STOP BUTTON ON THE MACHINE!
This will cut the power to the entire machine and will stop everything.

Things to consider when creating GCODE
Basics
- Stock : The material you are using to create your workpiece from.
- Stock surface : is the top of your stock Z=0 or is or the bed Z=0 ?
- Clearance plane / Clearance height : This is the height of the Z-Axis at
  which the machine can move freely without hitting anything.
- Depth increment : Number of mm to cut at every pass.
- target depth / Final depth : The cutting operation continues to this depth.
  this depends on the Z=0. If the top of the stock is Z=0 then this will be a
  negative value with a minimum of the negative stock thickness.
  If the bed is Z=0 then this must never be a negative value.
- Cut feedrate / plunge feedrate : speed at which the spindle will move while
  cutting. This depends on the material and cutter used.
- Holding tabs : for cutting out your workpiece from the stock while still
  holding them with small tabs which you can remove later.
- Lead-in-move : instead of plunging straight down, use an angle to dive in
  the workpiece. This is better for the cutter and leaves less marring on the
  workpiece.
- Cut width : when making deep cuts (deeper than the cutter diameter), use
  extra cut width to create room for the chips to clear.
- Stepover : the amount of the cutter diameter that is taken off the material
  each pass when the cut width is wider then the cutter diameter. 0.4 is
  standard and works fine.
- Tool diameter: the diameter of the cutting part of the cutter. The shank that
  mounts in the spindle can be wider.
- Tool profile : e.g. endmill (straight), ballnose (round) or v-cutter (pointy)

Advanced :
- Roughing / finishing : roughing is to remove a lot of material fast,
  finishing is the final pass
- Roughing clearance : the amount of mm to leave sideways with this pass
  so you can clean it up with the finishing pass.
- Final depth increment : Number of mm to cut at the last pass. If you take a
   very light cut (0,1mm) at the end this will polish the complete cut.
- Corner over-cut : creates circles in straight corners
- Milling direction : Climb milling will force the tool away from the
  workpiece and will generate more vibrations in the machine but will
  prevent double cutting of chips resulting in a better surface finish.
  Conventional milling will pull the cutter towards the workpiece and will
  give a steadier stability but the cut does not have the best finish. When in
  doubt, choose the default, which is conventional.